## Slide 1
Suhag University Steel Bridges
Faculty of Eng. نموذج اختبار استرشادي 2020
Civil Eng. Dept. Time 3 hours
A deck type roadway steel bridge of overall span 18 ms is supported on two main girders as shown in Fig. 1. The longitudinal beams are spaced at 3 m between center lines. The stringers are supported on the cross girders. The cross girders are spaced 3.0 m apart as shown in the cross-section Fig. 2.
Given data :-
Own weight of reinforced concrete and cover =800 kg/m2
Live loads as mentioned in the Egyptian code truck 60 t and truck 40 t in addition to a uniform distributed loads .
Spacing between cross girders =3.0 m
Use bolts 24 mm diameter.
Thickness of gusset plates = 12 mm, Steel used 36/52.
Required:-
Calculate the absolute B.M. and Absolute S.F for an intermediate stringer.
Calculate the absolute B.M. and Absolute S.F for an intermediate cross-girder, then find out the suitable riveted cross-section.
Design the required connection between the stringer and X-girder beams, draw the connection using scale 1-10.
Find a suitable Built-Up welded cross-section for the intermediate Main Girder at the position of Maximum Bending Moment.
At point b, calculate the required stiffener, then check the stability of web plate.
Exact calculations with neat drawings scale 1/10 are appreciated
Best wishes
Dr Fawzy El_Behairy
June 2020

## Slide 2
Best wishes
Dr Fawzy El_Behairy
June 2020
15 3 m
Fig. 1
6 1 6 ms
Fig. 2
Aaaaaaaaaaaaaaaaaaaaaa
Aaaaaaaaaaaaaaaaaaaaaaaa
aaaaaaaaaaaaaaaaa
Aaaaaaaaaaaaaaaaaaaaaa
Aaaaaaaaaaaaaaaaaaaaaaaa
aaaaaaaaaaaaaaaaa
Suhag University Steel Bridges
Faculty of Eng. نموذج اختبار استرشادي 2020
Civil Eng. Dept. Time 3 hours
X Girder Stringers
12 ms
a b c